## Slide 1: Noise and Vibration Hazards

## Slide 2: Noise
 Sound is any change in pressure that can be detected by ear.
 Noise is defined as: Noise is unwanted or damaging sound that may damage our hearing
 Sound or a sound that is loud, unpleasant, unexpected, or undesired.
 By product of many industrial processes (ex. operating machinery)
Word ‘NOISE’ derived from latin word ‘NAUSEA’ which means feeling sickness
Noise is a type of sound which:-
  Caries no information
  Random
  Undesirable & Unwanted

## Slide 3: MEASURMENT OF NOISE
‘DECIBEL’(dB): The unit used to express the intensity of sound
Measuring Instruments :-
  1. Noise Dosimeter : for measuring mainly of industrial noise(personal noise exposure level)
  2. Sound level meter: which measures the intensity of sound in dB (area noise level)
  3. Octave-band frequency analyzer: which measures the noise inoctave bands
   Noise Mapping (Area Monitoring) Simple Dosimeter

## Slide 4
A noise dosimeter (American English) or noise dosemeter (British English) is a specialized sound level meter intended specifically to measure the noise exposure of a person integrated over a period of time
Noise dosimeters measure and store sound pressure levels (SPL) and, by integrating these measurements over time, provide a cumulative noise-exposure reading for a given period of time, such as an 8-hour workday.
Dosimeters can function as personal or area noise monitors. In occupational settings, personal noise dosimeters are often worn on the body of a worker with the microphone mounted on the middle-top of the person’s most exposed shoulder

## Slide 5
A sound level meter is used for acoustic (sound that travels through air) measurements. It is commonly a hand-held instrument with a microphone. The best type of microphone for sound level meters is the condenser microphone, which combines precision with stability and reliability. The diaphragm of the microphone responds to changes in air pressure caused by sound waves. That is why the instrument is sometimes referred to as a Sound Pressure Level (SPL) Meter. This movement of the diaphragm, i.e. the sound pressure deviation (pascal Pa), is converted into an electrical signal (volts V). While describing sound in terms of sound pressure (Pascal) is possible, a logarithmic conversion is usually applied and the sound pressure level is stated instead, with 0 dB SPL equal to 20 micro pascals.
octave band frequency analyzer
When more detailed information about a complex sound is needed, the frequency range of 20Hz to 20kHz can be split into sections or bands. This is done electronically within a sound level meter.
These bands usually have a bandwidth of one octave or one third octave. More advanced instruments may be able to give a narrow band analysis of the noise data. This may be an FFT (Fast Fourier Transform) or information in 1/12 octaves.
An octave band is a frequency band where the highest frequency is twice the lowest frequency.
For example, an octave filter with a centre frequency of 1kHz has a lower frequency of 707Hz and an upper frequency of 1.414kHz. Any frequencies below and above these limits are rejected. A third octave has a width of 1/3 of that of an octave band.

## Slide 7: SOURCES OF NOISE
1-Stationary Sources:- Iron & Steel plants, Textile mills, Printing presses, Workshops, Metal Industries, use of loudspeakers on festivals, Elections, Worships in Temples, Mosques etc
2-Mobile Sources:- Road traffic, Railway traffic, Aero traffic, Marine vehicles, Agriculture machines

## Slide 8: OCCUPATIONAL NOISE
 “Noise related to any occupation is called OCCUPATIONAL NOISE”
 Working in maintenance shops or repairing buses involves using loud machinery such as motors, grinders, saws, presses, pneumatic equipment and hand held tools can also generate high noise levels.
 Ex- Cement & Concrete industries, Printing press, Sheet Metal industries, Gear manufacturing plants, Construction sites

## Slide 9: EFFCTS OF OCCUPATIONAL NOISE
 Physiological Effects
  a) Hearing impairment
  b) Hypertension
  c) Heart disease
  d) Lowering the concentration and effect on memory
  e) Muscular strain and nervous breakdown.
 Psychological Effects
  a) Depression and Fatigue
  b) Mental Stress
  c) Frustration
  d) Sleep Interference

## Slide 10: AUDITORY EFFECTS
Temporary hearing loss occurs when sound vibrations are blocked from reaching the inner ear. This may be due to wax buildup, an infection of the middle ear, or explosive sounds that damage the eardrum or middle ear. This type of hearing loss is reversible. The ear may recover on its own or it may be surgically corrected.
Permanent hearing loss occurs when cells and nerves in the inner ear are damaged. Individuals don’t realize they are experiencing hearing loss because it happens gradually. It cannot be corrected or reversed.

## Slide 11: CONTROL OF NOISE: Engineering control
Substitution: Replace noisy equipment with quieter
Modification: Modify the way in which the equipment operates so that it generates less noise.
Isolation: Having them work in enclosed room. Segregate noisy areas with sound barriers
Maintenance: Maintenance of equipment and the engineering controls that have been implemented is very important or the improvements in noise level will be lost Administrative control
Rotating work schedules: purposely to have amount of time that a worker is exposed to noise is within acceptable limits
Provision of training: Noise awareness training
Warning sign: Warning sign at all entrances to the high noise area

## Slide 12
Conducting Audiometric test: A test to determine employees hearing threshold or ability
Providing appropriate PPE: if reductions in noise level and exposure time have not reduced, then appropriate hearing protection must be provided according to the standard

## Slide 13: Vibration Hazards

## Slide 14: VIBRATION
Vibration is the mechanical oscillations of an object about an equilibrium point. The oscillations may be regular such as the motion of a pendulum .

## Slide 15: How does the vibration exposure Occur ?
Contact with a vibrating machine transfer vibrating energy to a person’s body.
Depending upon the exposure, it affect a major part of the workers body or organ.
Each organ of the body has its own resonant frequency. If exposure occur at or near to these resonant frequencies, the resulting effect is greatly increased.
For occupational health the exposures to hand-arm vibrations and whole- body vibrations are concerns.

## Slide 16: TYPES OF VIBRATIONS
Based on force applied:-
    1. Free vibration -Occurs when a mechanical system is set off with an initial input and then allowed to vibrate freely. Ex-simple pendulum
    2. Forced vibration -When a time-varying disturbance (load, displacement or velocity) is applied to a mechanical system. Ex-shaking washing machine due to an imbalance, transportation vibration (caused by truck engine, springs, road, etc.)
Based on vibration expose
    Hand Arm Vibration(HAV)- When hand of a worker is exposed to vibrating body during the occupation.
    Whole Body Vibration(WBV)- when whole body expose to vibrating body or system.
    Environmental Vibration

## Slide 18: Measurement of Vibration Exposure
Measurement of vibration includes three parameters :
    1. The vibration amplitude (Acceleration), which is the characteristic to describe the severity of the vibration.
    2. Frequency spectrum
    3. Duration of Exposure
Vibration Measurement System
A Typical Vibration System consist of :
    A transducer( convert mechanical to electrical energy) to sense the vibration .( Suitable transducers for human vibration measurement is the Accelerometer)
    A pre-amplifying device
    Frequency weighing filter( to allow for the variation of human response to vibration of different frequencies & compared the measured vibration with standards)
    Tape recorder to collect information for further analysis
    Signal analyzer to obtain relevant parameters like acceleration and peak values

## Slide 19: Transducers
Vibration is usually is measured using accelerometers housed in mounts so they do not compress the seat or distort the posture too much.
A "seat transducer", comprising a deformable pad that follows the seat contour and containing a tri-axial accelerometer for simultaneous measurements in three axes of vibration, is commonly used these days.
This seat transducer is placed on a seat with a driver sitting on it or is strapped either to the driver' back or the seat back-rest.

## Slide 20
To measure whole-body vibration transmitted through the floor, the seat transducer is placed on the floor with a small weight on top to ensure a good contact between the floor and the transducer

## Slide 21: Vibration Meter
It measures magnitude of vibration as accelerations at different frequencies and directions using a transducer, amplifier and recorder.
The acceleration is measured using a transducer located at the source of vibration or area through which the vibration is transmitted.

## Slide 23: Effects of Vibration Exposure
Vibration can cause annoyance and noise to human body and physical damage to machines and structures.
Effects of vibration are feeling of disoriented or displacement, giddiness, sickness, vibration disease and sometimes fatal.
Whole body vibration can cause permanent damage to body or abdominal, spinal and bone damage.
  At low frequencies( up to 10Hz) the vibrations propagate through the entire body regardless of the location of in put.
  In case of high frequency vibration, the zone of propagation is limited by the area of contact causing vascular disorder in that part
  Low frequency vibration(3-6 Hz)=effects the chest region and create the feelings of Nausea
  20-30 Hz frequency region resonance effect on head, neck and shoulders
  60-90 Hz frequency effect the eye ball
  100-200 Hz frequency effect on lower jaw and skull system

## Slide 24: Effects on Human body
Whole body vibration may cause
1. Increase in oxygen consumption.
2. Increase in pulmonary ventilation and cardiac output. Affects CNS, damages internal organs.
3. Difficulty in maintaining steady posture.
4. Effects on visual acuity and narrows the field of vision.
5. Marked changes in bone structure – • Spondylities. • Deformations. • Intervertebral Osteochondrosis. • Calcification of the intervertebral disc.

## Slide 25
6. Blood changes - • hypoglycaemia. • hypocholesteremia. • low ascorbic acid levels.
7. Alternations in the electrical activity of the brain.
8. Effects on endocrine, biochemical and histopathologic systems of the body.
It causes numbness and blanking of the fingers with probable loss of muscular control and reduction of sensitivity to heat ,cold or pain. It causes paleness of the skin due to oxygen deficiency. All vibration make us tired or irritable.

## Slide 26
Raynaud's phenomenon is a condition resulting in discoloration of the fingers and/or the toes after exposure to changes in temperature (cold or hot) or emotional events. Skin discoloration occurs because an abnormal spasm of the blood vessels causes a diminished blood supply to the local tissues.

## Slide 27: Vibration control measures
Include technical, organisational, hygienic, prophylactic and therapeutic measures.
Technical or engineering measures include automation, remote control and eliminating or reducing vibration from the design stage or at source.
Organisation measures include good preventive and corrective maintenance and arrangement of work schedules in such a way to decrease time of exposure.
Prophylactic and therapeutic measures – pre-employment and periodical medical examinations play an important role. Special gymnastics, hydrotherapeutic procedures, massage and UV radiation can prevent further development of vibration disease and preserve working capacity.
Special vibration absorbing handles fitted to hand tools, springs, suspension seats and shock absorbers are useful.
Reduction in exposure time. Rotate vibrative job and introduce rest schedules so that individual exposure is shortened.
Personal precautions include watching for symptoms, to apply loose grip, to wear gloves and footwear with shock-absorbing soles to damp vibration to use PPE and to get medical attention.
Automation and remote control system.

## Slide 28: Technical measures
Anti Vibration Tools  Certain manufacturing Company produce anti vibration tools such as anti vibration pneumatic chipping hammers, pavement breakers, and vibration damped pneumatic riveting guns.
Anti Vibration Gloves  Anti vibration Gloves are made using a layer of viscoelastic material. Measurement have shown that such gloves have limited effectiveness in absorbing low frequency vibration, the major contributor to vibration related disorders , hence they have little effect on vibration induced finger syndrome, however gloves helps from cuts and abrasions and cold temperatures
Vibration Damping  Vibration dampers(absorption) are used under machine foundation & machine should be installed in such a way that dampers come in contact between the building foundation & machine.
Remote control vibratory plate Operator vibration exposure – Zero
Mechanization removes the risk Machine-mounted pick replaces hand- operated breakers
Demolition without vibration Use hydraulic crushers instead of demolition hammers