## Slide 1: Water Pollution

## Slide 2: According to the Water (Prevention and Control of Pollution) Act, 1974, ―
water pollution means such contamination of water or such alteration of the physical, chemical or biological properties of water or such discharge of any sewage or trade effluent or of any other liquid, gaseous or solid substance into water (whether directly or indirectly) as may or is likely to, create a nuisance or render such water harmful or injurious to public health or safety or to domestic, commercial, industrial, agricultural or other legitimate uses, or the life and health of animals or plants or of aquatic organisms.

## Slide 3: Classification of pollutants

## Slide 4: Causes of water pollution
Growing Population
  Every year we add millions of people to the world population and our country is no exception. The earth is now overcrowded and consumption habit of the people is on the rise. The growth of population gave rise to increase in wants and demands of mankind and has succeeded in creating acute problem of water pollution.

## Slide 5
Industrialization
  Rapid industrialization is another cause of worry as far as water pollution is concerned. Immediately after the independence, major steps were taken in our country in its stride for development in order to give its economy a big push.
  Industrialization along with development brought with it a danger to the human civilization- the problem of environmental pollution

## Slide 6
Urbanization
  big cities also developed just near the water courses particularly besides the big rivers subsequently attracted the establishment of industrial and commercial basis in and around the cities.
  Since many towns and cities lack a proper sewerage system, the condition worsened further.

## Slide 7
Nature of Modern Technology
  The nature of productive technology in recent years has been largely responsible for the generation of synthetic and non biodegradable substances such as plastics, chemical nitrogen fertilizers, synthetic detergents, synthetic fibres, petrochemical and other environmentally injurious industries and ―disposable culture.

## Slide 8
Modern Agricultural Practices
  Fertilizers like phosphates and nitrates cause wide spread damage when applied carelessly to crops. The fertilizers can be transmitted to ground water by leaching and to surface waters by natural drainage and storm run-off.
  In addition to fertilizers various kinds of pesticides and insecticide also applied. Almost all the pesticides those are used are toxic to human and animals
Click to add text

## Slide 9: SOURCES OF WATER POLLUTION
1, Domestic wastes
2. Industrial wastes
3. Agricultural wastes, insecticides and pesticides
4. Thermal pollution
5. Marine pollution and
6. Radioactive wastes.

## Slide 10: Type of Pollutants Oxygen-Demanding Substances
Dissolved oxygen is a key element in water quality that is necessary to support aquatic life.
A demand is placed on the natural supply of dissolved oxygen by many pollutants in wastewater. This is called biochemical oxygen demand, or BOD,
Organic matter and ammonia are “oxygen-demanding” substances. Oxygen-demanding substances are contributed by domestic sewage and agricultural and industrial wastes of both plant and animal origin, such as those from food processing, paper mills, tanning, and other manufacturing processes.
These substances are usually destroyed or converted to other compounds by bacteria if there is sufficient oxygen present in the water, but the dissolved oxygen needed to sustain fish life is used up in this break down process.

## Slide 11: Pathogens
Infectious micro-organisms, or pathogens, may be carried into surface and groundwater by sewage from cities and institutions, by certain kinds of industrial wastes, such as tanning and meat packing plants, and by the contamination of storm runoff with animal wastes from pets, livestock and wild animals, such as geese or deer.
Humans may meet these pathogens either by drinking contaminated water or through swimming, fishing, or other contact activities.
Modern disinfection techniques have greatly reduced the danger of waterborne disease.

## Slide 12: Nutrients
Carbon, nitrogen, and phosphorus are essential to living organisms and are the chief nutrients present in natural water. Large amounts of these nutrients are also present in sewage, certain industrial wastes, and drainage from fertilized land.
Conventional secondary biological treatment processes do not remove the phosphorus and nitrogen to any substantial extent -- in fact, they may convert the organic forms of these substances into mineral form, making them more usable by plant life.
When an excess of these nutrients overstimulates the growth of water plants, the result causes excessive growth of algae. Uncontrolled algae growth blocks out sunlight and chokes aquatic plants and animals by depleting dissolved oxygen in the water at night.
The release of nutrients in quantities that exceed the affected waterbody’s ability to assimilate them results in a condition called eutrophication.

## Slide 13: Inorganic and Synthetic Organic Chemicals
A vast array of chemicals are included in this category. Examples include detergents, household cleaning aids, heavy metals, pharmaceuticals, synthetic organic pesticides and herbicides, industrial chemicals, and the wastes from their manufacture.
Many of these substances are toxic to fish and aquatic life and many are harmful to humans. Some are known to be highly poisonous at very low concentrations. Others can cause taste and odor problems, and many are not effectively removed by conventional wastewater treatment.

## Slide 15: Thermal
Heat reduces the capacity of water to retain oxygen.
In some areas, water used for cooling is discharged to streams at elevated temperatures from power plants and industries. Even discharges from wastewater treatment plants and storm water retention ponds affected by summer heat can be released at temperatures above that of the receiving water, and elevate the stream temperature.
Unchecked discharges of waste heat can seriously alter the ecology of a lake, a stream, or estuary.