## Slide 1
Applying Shockley’s Equation
The transfer curve can also be obtained directly from Shockley’s equation given simply the values of IDSS and VP.
The levels of IDSS and VP define the limits of the curve on both axes and leave only the necessity of finding a few intermediate plot points.
Substituting VGS = 0 V gives
Substituting VGS = VP yields
substitute VGS=1 V,
Note the care taken with the negative signs for VGS and VP in the calculations above.
So for a given IDSS and VP (as is normally provided on specification sheets) the level of ID can be found for any level of VGS.
Also the resulting level of VGS for a given level of ID

## Slide 2
FET PARAMETERS
The gate-to-source voltage controls the drain-to-source (channel) current of an FET.
A dc gate-to-source voltage controlled the level of dc drain current through a relationship known as Shockley’s equation:
ID = IDSS(1 - VGS/VP)2
The change in current that will result from a change in gate-to-source voltage can be determined using the transconductance, gm in the following manner:
The root word conductance was chosen for gm because it is determined by a voltage-to-current ratio similar to the ratio that defines the conductance of a resistor
G = 1/R = I/V.
The prefix trans- in the terminology applied to gm reveals that it establishes a relationship between an output and input quantity
Solving for gm from above Eq. we have

## Slide 3
FET Output Impedance rd
The output impedance is defined on the characteristics of Fig. as the slope of the horizontal characteristic curve at the point of operation.
The more horizontal the curve, the greater the output impedance.
If perfectly horizontal, the ideal situation is on hand with the output impedance being infinite (an open circuit)—an often applied approximation.
In equation form,
Note that the voltage VGS remain constant when rd is determined.
Voltage gain Av or Amplification factor (µ)
or
so that
If rd > 10RD:

## Slide 5
MOSFET (metal-oxide-semiconductor-field-effect transistor )
There are two types of FETs: (i) JFETs and (ii) MOSFETs.
MOSFETs are further broken down into
(i) depletion type and
(ii) enhancement type.
Label MOSFET stands for Metal-Oxide-Semiconductor-Field-Effect Transistor.
The terms depletion and enhancement define their basic mode of operation,
Depletion MOSFET : Basic Construction
The basic construction of the n-channel depletion-type MOSFET is provided in Fig.
A slab of p-type material is formed from a silicon base and is referred to as the substrate.
It is the foundation upon which the device will be constructed.
In some cases the substrate is internally connected to the source terminal.
However, many discrete devices provide an additional terminal labeled SS, resulting in a four-terminal device such as that appearing in Fig.

## Slide 6
The source and drain terminals are connected through metallic contacts to n-doped regions linked by an n-channel as shown in the figure.
The gate is also connected to a metal contact surface
but remains insulated from the n-channel by a very thin silicon dioxide (SiO2) layer.
SiO2 is a particular type of insulator referred to as a dielectric
Sets up opposing electric fields within the dielectric when exposed to an externally applied field.
The fact that the SiO2 layer is an insulating layer reveals the following fact
There is no direct electrical connection between the gate terminal and the channel of a MOSFET.
In addition
It is the insulating layer of SiO2 in the MOSFET construction that accounts for the very desirable high input impedance of the device.
The insulating layer between the gate and channel has resulted in another name for the device: insulated gate FET or IGFET

## Slide 7
Basic Operation and Characteristics
In Fig. the gate-to-source voltage is set to zero volts by the direct connection from gate-to-source, and
a voltage VDS is applied across the drain-to-source terminals.
The result is an attraction for the positive potential at the drain by the free electrons of the n-channel and a current similar to that established through the channel of the JFET.
The resulting current with VGS = 0 V continues to be labeled as IDSS, as shown in Fig in next slide
In Fig. b, VGS set at a negative voltage VGS = 1V.
The negative potential at the gate will tend to pressure electrons toward the p-type substrate (like charges repel) and attract holes from the p-type substrate (opposite charges attract)
Depending on the magnitude of the negative bias established by VGS, a level of recombination between electrons and holes will occur that will reduce the number of free electrons in the n-channel available for conduction.
The more negative the bias, the higher the rate of recombination.

## Slide 8
Characteristic curve for MOSFET

## Slide 9
The resulting level of drain current is therefore reduced with increasing negative bias for VGS as shown in Fig. for VGS =1 V, 2 V, and so on, to the pinch-off level of 6 V.
The resulting levels of drain current and the plotting of the transfer curve proceeds exactly as for the JFET.
For positive values of VGS, the positive gate will draw additional electrons (free carriers) from the p-type substrate due to the reverse leakage current and
Establish new carriers through the collisions resulting between accelerating particles.
As the gate-to-source voltage continues to increase in the positive direction, Fig. reveals that the drain current will increase at a rapid rate.
One must be aware of the maximum drain current rating since it could be exceeded with a positive gate voltage.
So, the application of a positive gate-to-source voltage has “enhanced” the level of free carriers in the channel compared to that encountered with VGS= 0 V.
For this reason the region of positive gate voltages on the drain or transfer characteristics is often referred to as the enhancement region,
with the region between cutoff and the saturation level of IDSS referred to as the depletion region.
Shockley’s equation applicable for the depletion-type MOSFET characteristics in both the depletion and enhancement regions.
For both regions, it is simply necessary that the proper sign be included with VGS in the equation and the sign be carefully monitored in the mathematical operations.

## Slide 10
p-Channel Depletion-Type MOSFET
The construction of a p-channel depletion-type MOSFET is exactly the reverse of n-channel depletion-type MOSFET .
That is, there is now an n-type substrate and a p-type channel, as shown in Fig. a.
The terminals remain as same (D,S,G), but all the voltage polarities and the current directions are reversed, as shown in the same figure.
The drain characteristics would appear exactly as in Fig. for n-channel depletion-type MOSFET but with VDS having negative values,
ID having positive values as indicated (since the defined direction is now reversed) and
VGS having the opposite polarities as shown in Fig. c in next slide.
The reversal in VGS will result in a mirror image (about the ID axis) for the transfer characteristics as shown in Fig. b in next slide.
In other words, the drain current will increase from cutoff at VGS = VP in the positive VGS region to IDSS and then continue to increase for increasingly negative values of VGS.
Shockley’s equation is still applicable and requires simply placing the correct sign for both VGS and VP in the equation

## Slide 11
Transfer Characteristics : p-Channel depletion-type MOSFET with IDSS = 6mA and VP =6 V

## Slide 12
Symbols
The graphic symbols for an n- and p-channel depletion-type MOSFET are provided in Fig.
Here the lack of a direct connection (due to the gate insulation) between the gate
and channel is represented by a space between the gate and the other terminals of the
symbol.
The vertical line representing the channel is connected between the drain and source and is “supported” by the substrate.
Two symbols are provided for each type of channel to reflect the fact that in some cases the substrate is externally available while in others it is not.
For mostly for the analysis the substrate and source will be connected and the lower symbols is employed.
The device appearing in Fig. has three terminals, with the terminal identification
appearing in the same figure.
The specification sheet for a depletion-type MOSFET is similar to that of a JFET.
The levels of VP and IDSS are provided along with a list of maximum values and typical “on” and “off” characteristics.

## Slide 14
ENHANCEMENT-TYPE MOSFET : Basic Construction
The basic construction of the n-channel enhancement-type MOSFET is provided in Fig.
A slab of p-type material is formed from a silicon base and is again referred to as the substrate.
As with the depletion-type MOSFET, the substrate is some-times internally connected to the source terminal,
while in other cases fourth lead is made available for external control of its potential level.
The source and drain terminals are again connected through metallic contacts to n-doped regions, but note in Fig. the absence of a channel between the two n-doped regions.
This is the primary difference between the construction of depletion-type and enhancement-type MOSFETs—
the absence of a channel as a constructed component
of the device.
The SiO2 layer is still present to isolate the gate metallic platform from the region between the drain and source,
but now it is simply separated from a section of the p-type material.
In summary, therefore, the construction of an enhancement-typeMOSFET is quite similar to that of the depletion-type MOSFET except for the absence of a channel between the drain and source terminals.

## Slide 15
Basic Operation and Characteristics
If VGS = 0 V and a voltage applied between the drain and source of the device of Fig.
the absence of an n-channel will result in a current of effectively zero amperes
Quite different from the depletion-type MOSFET and JFET where ID = IDSS.
It is not sufficient to have a large accumulation
of carriers (electrons) at the drain and source
(due to the n-doped regions)
if a path fails to exist between the two with VDS some positive voltage, VGS at 0 V, and terminal SS directly connected to the source, there are in fact two reverse-biased p-n junctions between the n-doped regions and the p-substrate to oppose any significant flow between drain and source.

## Slide 16
In Fig. both VDS and VGS have been set at some positive voltage greater than 0 V, establishing the drain and gate at a positive potential with respect to the source.
The positive potential at the gate will pressure the holes (since like charges repel) in
the p-substrate along the edge of the SiO2 layer to leave the area and enter deeper regions of the p-substrate, as shown in the figure.
The result is a depletion region near the SiO2 insulating layer void of holes.
However, the electrons in the p-substrate (the minority carriers of the material) will be attracted to the positive gate and accumulate
in the region near the surface of the SiO2 layer.
The SiO2 layer and its insulating qualities will prevent the negative carriers from being absorbed at the gate terminal.
As VGS increases in magnitude, the concentration of electrons near the SiO2 surface increases until eventually the induced n-type region can support a measurable flow between drain and source.
The level of VGS that results in the significant increase in drain current is called the threshold voltage and is given the symbol VT

## Slide 17
On specification sheets it is referred to as VGS(Th),.
Since the channel is nonexistent with VGS = 0 V and “enhanced” by the application of a positive gate-to-source voltage, this type of MOSFET is called an enhancement-type MOSFET.
Both depletion- and enhancement-type MOSFETs have enhancement-type regions, but the label was applied to the latter since it is its only mode of operation.
As VGS is increased beyond the threshold level, the density of free carriers in the induced channel will increase, resulting in an increased level of drain current.
However, if we hold VGS constant and increase the level of VDS, the drain current will
eventually reach a saturation level as occurred for the JFET and depletion-type MOSFET.
The leveling off of ID is due to a pinching-off process depicted by the narrower channel at the drain end of the induced channel as shown in Fig in next slide.
Applying Kirchhoff’s voltage law to the terminal voltages of the MOSFET of Fig., we find that

## Slide 19
If VGS is held fixed at some value such as 8 V and VDS is increased from 2 to 5 V, the voltage VDG will drop from 6 to 3 V and the gate will become less and less positive with respect to the drain.
This reduction in gate-to-drain voltage will in turn reduce the attractive forces for free carriers (electrons) in this region of the induced channel, causing a reduction in the effective channel width.
Eventually, the channel will be reduced to the point of pinch-off and a saturation condition will be established as described earlier for the JFET and depletion-type MOSFET.
In other words, any further increase in VDS at the fixed value of VGS will not affect the saturation level of ID until breakdown conditions are encountered.
The drain characteristics of Fig. reveal that for the device of Fig. with VGS = 8 V, saturation occurred at a level of VDS = 6 V.
In fact, the saturation level for VDS is related to the level of applied VGS by
Obviously, therefore, for a fixed value of VT , then the higher the level of VGS, the more the saturation level for VDS, as shown in Fig. in next slide by the locus of saturation levels.

## Slide 21
For the characteristics of Fig. the level of VT is 2 V, as revealed by the fact that the drain current has dropped to 0 mA.
In general, therefore:
For values of VGS less than the threshold level, the drain current of an enhancement- type MOSFET is 0 mA.
Figure clearly reveals that as the level of VGS increased from VT to 8 V, the resulting saturation level for ID also increased from a level of 0 to 10 mA.
In addition, it is quite noticeable that the spacing between the levels of VGS increased as the magnitude of VGS increased, resulting in ever-increasing increments in drain current.
For levels of VGS = VT , the drain current is related to the applied gate-to-source voltage by the following nonlinear relationship:
The k term is a constant that is a function of the construction of the device. The value of k can be determined from the following equation

## Slide 22
The transfer curve of Fig. is certainly quite different from those obtained earlier.
For an n-channel (induced) device, it is now totally in the positive VGS region and does not rise until VGS = VT.