## Slide 13
Junction Field-effect Transistor (JFET)
The field-effect transistor (FET) is a three-terminal device used for a variety of application just like BJT.
Although there are some important differences between the FET and BJT, together with many similarities.
The primary difference between the two types of transistors is the fact that
The BJT transistor is a current-controlled device, while the JFET transistor is a voltage-controlled device.
In other words, In BJT the current IC is a direct function of the level of IB.
For the FET the current ID will be a function of the voltage VGS applied to the input circuit
In each case the current of the output circuit is being controlled by a parameter of the input circuit—in one case a current level and in the other an applied voltage.
Field-effect transistor amplifiers provide an excellent voltage gain with the added feature of a high input impedance.
They are also considered low-power consumption configurations with good frequency range and minimal size and weight.
For FET ac equivalent model is somewhat simpler than that employed for BJTs.
The BJT had an amplification factor (beta), the FET has a transconductance factor, gm.

## Slide 14
Just as there are npn and pnp bipolar transistors, there are n-channel and p-channel
field-effect transistors.
However, the BJT transistor is a bipolar device whereas the FET is a unipolar device depending solely on either electron (n-channel) or hole (p-channel) conduction.
For the FET an electric field is established by the charges present that will control the conduction path of the output circuit without the need for direct contact between the controlling and controlled quantities.
One of the most important characteristics of the FET is its high input impedance. At a level of 1M to several hundred megohms. it far exceeds the typical input resistance levels of the BJT transistor configurations.
Although the BJT transistor has a much higher sensitivity to changes in the applied signal than FET.
In other words, the variation in output current is typically a great deal more for BJTs
than FETs for the same change in applied voltage.
For this reason, typical ac voltage gains for BJT amplifiers are a great deal more than for FETs.
FETs are more temperature stable than BJTs
FETs are usually smaller in construction and easy to fabricate in IC than BJTs,
So FET’s are particularly useful in integrated-circuit (IC) chips.
Comparison of BJT and FET
There are two types of FETs:
JFETs and
MOSFETs

## Slide 15
BASIC CONSTRUCTION OF THE N-CHANNEL JFET
FET is a three terminal device (Source S, Drain D, Gate G)
In RHS Figure the top of the n-type channel is connected through an ohmic contact to a terminal referred to as the drain (D)
while the lower end of the same material is connected through an ohmic contact to a terminal referred to as
the source (S).
The two embedded p-type materials are connected toge-ther and to the an ohmic contact referred to as gate (G) terminal.
Therefore, the drain and source are connected to the ends of the n-type channel and the gate to the two layers of p-type material.
The basic construction of the n-channel JFET is shown in Fig.
The major part of the structure is the n-type material (referred as substrate)
within substrate a channel of majority charge carrier, electron forms between the embedded layers of p-type material

## Slide 16
As shown in Prev. fig, in the absence of any applied potentials the JFET has two p-n junctions under no-bias conditions.
The result is a depletion region at each junction that resembles the same region of a diode under no-bias conditions.
CHARACTERISTICS OF JFETs
Recall also that a depletion region is that region void of free carriers and therefore unable to support conduction through the region.
the water analogy of Fig RHS is appropriate and does provide a sense for the JFET control at the gate terminal and the appropriateness of the terminology applied to the terminals of the device.
The source of water pressure can be likened to the applied voltage from drain to source that will establish a flow of water (electrons) from the spigot (source).
The “gate,” through an applied signal (potential), controls the flow of water (charge) to the “drain.”
The drain and source terminals are at opposite ends of the n-channel as introduced in Prev. Fig. because the terminology is defined for electron flow.

## Slide 17
JFET CHARACTERISTICS
VGS = 0 V,
(i) VDS Some Positive Value
In Fig., a positive voltage VDS has been applied across the channel and
gate has been connected directly to the source to establish the condition VGS = 0 V.
The result is a gate and source terminal at the same potential and
a depletion region exists in the low end of each p-material similar to the distribution of the no-bias conditions of Fig.
(ii) The instant the Drain voltage VDD ( VDS) is applied: The electrons will be drawn to the drain terminal, establishing the conventional current ID with the defined direction of Fig
The path of charge flow clearly reveals that the drain and source currents are equivalent (ID = IS). Under the conditions appearing in Fig. RHS,
the flow of charge is relatively uninhibited and limited solely by the resistance of the n-channel between drain and source.
Construction and Characteristics of JFETs

## Slide 18
The current ID will establish the voltage levels through the channel as indicated in the figure.
The result is that the upper region of the p-type material will be reverse biased by about 1.5 V, with the lower region only reverse-biased by 0.5 V.
(iii) Greater the applied reverse bias: The wider the depletion region—hence the distribution of the depletion region as shown in Fig.
The fact that the p-n junction is reverse-biased for the
length of the channel results in a gate current of zero amperes as shown in the same figure.
Fact that IG = 0 A is an important characteristic of the JFET.
It is important to note that the depletion region is wider near the top of both p type materials.
To understand the reason for the change in width of the depletion region
Assuming a uniform resistance in the n-channel, the resistance of the channel can be broken down to the divisions appearing in Fig.
As the voltage VDS is increased from 0 to a few volts: the current will increase as determined by Ohm’s law and the plot ID versus VDS is shown in RHS
The relative straightness of the plot reveals that for the region of low values of VDS, the resistance is essentially constant.
As VDS increases and approaches a level referred to as VP in plot the depletion regions
will widen  causing a noticeable reduction in the channel width.
The reduced path of conduction causes the resistance to increase.

## Slide 19
The more horizontal the curve, the higher the resistance, suggesting that the resistance is approaching “infinite” ohms in the horizontal region.
This fact that ID does not drop off at pinch-off and
maintains the saturation level is verified by the following fact:
The absence of a drain current would remove the possibility of different potential levels through the n-channel material to establish the varying levels of reverse bias along the p-n junction.
 The result would be a loss of the depletion region distribution that caused pinch-off
If VDS is increased to a level where it appears that the two depletion regions would “touch” as shown in Fig. a condition referred to as pinch-off will result.
The level of VDS that establishes this condition is referred to as the pinch-off voltage and is denoted by VP
In actuality, the term pinch-off is a misnomer in that it suggests the current ID is pinched off and drops to 0 A As shown in Fig.
however, this is hardly the case— actually at and after pinch off ID maintains a saturation level defined as IDSS in Fig.
In reality a very small channel still exists at and after
pinch off with a current of very high density.

## Slide 20
JFET CHARACTERISTICS: VGS = 0

## Slide 21
As VDS is increased beyond VP ,
the “close channel region” encounter between the two depletion regions will increase in length along the channel,
but the level of ID remains essentially the same.
In essence, therefore, once VDS > VP the JFET has the characteristic of a current source.
the current is fixed at ID = IDSS, but the voltage VDS (for levels VP) is determined by the applied load.
IDSS term is derived from the fact that it is the Drain-to-Source current with a Short-circuit connection from gate to source.
IDSS is the maximum drain current for a JFET and is defined
by the conditions VGS > 0 V and VDS > |VP|.

## Slide 22
VGS < 0 V: The voltage from gate to source, VGS is the Controlling Voltage of the JFET.
Family of curves of ID - VDS for various levels of VGS can be obtained for the JFET, just as for the BJT for IC versus VCE for different levels of IB obtained for the BJT .
For the n-channel device the controlling voltage VGS is made more and more negative from its VGS = 0 V level. Means gate terminal will be set at lower & lower potential levels as compared to source
In Fig. negative voltage of -1 V has been applied between the gate and source terminals for a low level of VDS. 33
The effect of the applied negative-bias VGS is to establish depletion regions similar to those obtained with VGS = 0 V but at lower levels of VDS.
The result of applying a negative bias to the gate is
to reach the saturation level at a lower level of VDS as shown in Fig. for VGS= 1 V.
The resulting saturation level for ID has been reduced
And will continue to decrease as VGS is made more and more negative.
The pinch-off voltage continues to drop in a parabolic manner as VGS becomes more and more negative.
When VGS= - VP it will be sufficiently negative to establish a saturation level that is essentially 0 and
In this case for all practical purposes the device has been “turned off.”

## Slide 23
JFET CHARACTERISTICS: VGS < 0

## Slide 24
The level of VGS that results in ID = 0 mA is defined by VGS = VP, with VP being a
negative voltage for n-channel devices and a positive voltage for p-channel JFETs.
On most specification sheets the pinch-off voltage is specified as VGS(off) rather than VP.
The region to the right of the pinch-off locus is the region typically employed in linear amplifiers (amplifiers with minimum distortion of the applied signal) and is commonly referred to as the constant-current, saturation, or linear amplification region.

## Slide 31
VOLTAGE-CONTROLLED RESISTOR
The region to the left of the pinch-off locus of is referred to as the ohmic or voltage-controlled resistance region.
In this region the JFET can actually be employed as a variable resistor (possibly for an automatic gain control system) .
Whose resistance is controlled by the applied gate-to-source voltage.
The slope of each curve and therefore the resistance of the device between drain and source for VDS < VP is a function of the applied voltage VGS.
As VGS becomes more and more negative,
the slope of each curve becomes more and more horizontal, corresponding with an increasing resistance level.
The following equation will provide a good first approximation to the resistance level in terms of the applied voltage VGS.
Where
ro is the resistance with VGS = 0 V and rd the resistance at a particular level of VGS.
For an n-channel JFET with ro equal to 10 k (VGS = 0 V, VP =6 V), rd = 40k  at VGS =3 V.

## Slide 32
P-CHANNEL JFET DEVICES
The p-channel JFET is constructed in exactly the same manner as the n-channel device of Fig., but with a reversal of the p- and n-type materials as shown in Fig.
The defined current directions are reversed, as are the actual polarities for the voltages VGS and VDS.
For the p-channel device, the channel will be constricted by increasing positive voltages from gate to source and
VDS will result in negative voltages on the characteristics of Fig shown in next slide.
Which has an IDSS of 6 mA and a pinch-off voltage of VGS = +6 V.
Minus signs for VDS simply indicate that the source is at a higher potential than the drain.
Note at high levels of VDS , the curves suddenly rise to levels that seem unbounded.
The vertical rise is an indication that breakdown has occurred and
the current through the channel is now limited solely by the external circuit.
Although not appearing in Fig. for the n-channel device, they do occur for the n-channel device if sufficient voltage is applied.
This region can be avoided if the level of VDSmax is noted on the specificationsheet and
The design is such that the actual level of VDS is less than this value for all values of VGS.

## Slide 33
Charcteristic curve for P-CHANNEL JFET Devices

## Slide 34
JFET SYMBOLS
The graphic symbols for the n-channel and p-channel JFETs are provided in Fig. RHS
The arrow is pointing in for the n-channel device of Fig. a to represent the direction in which IG would flow if the p-n junction were forward-biased.
For the p-channel device (Fig.b) the only difference in the symbol is the direction of the arrow.
Important Points:-
The maximum current is defined as IDSS and occurs when VGS = 0 V and VDS ≥ |VP| as shown in Fig. a.
For gate-to-source voltages VGS less than (more negative than) the pinch-off level, the drain current ID = 0 A FET is cutoff Fig. b
For all levels of VGS between 0 V and the pinch-off level, the current ID will range between IDSS and 0 A, respectively, Fig. c
For p-channel JFETs a similar list can be developed.
Fig. a
Fig. b
Fig. c
n-channel

## Slide 35
TRANSFER CHARACTERISTICS OF JFET
In BJT, a linear relationship exists between IC and IB. output current IC and input controlling current IB were related by beta.
But unfortunately, this linear relationship does not exist between the output and input quantities of a JFET.
The relationship between ID and VGS in JFET is defined by Shockley’s equation:
The squared term of the equation will result in a nonlinear relationship between ID and VGS
Above equation produce a curve that grows exponentially with decreasing magnitudes of VGS.
a graphical rather than mathematical approach will in general be more direct and easier to apply.
The graphical approach, however, will require i)a plot of above Eq. to represent the device and a ii) plot of the network equation relating the same variables.
The solution is defined by the point of intersection of the two curves.
It is important to keep in mind when applying the graphical approach that the device characteristics will be unaffected by the network in which the device is employed.
The network equation may change along with the intersection between the two curves, but the transfer curve defined by Eq. is unaffected.

## Slide 36
Transfer curve (obtained using Shockley’s equation)
In Fig. two graphs are provided, with the vertical scaling in millamperes for each graph.
One is a plot of ID versus VDS, while the other is ID versus VGS.
Using the drain characteristics on the right of the “y” axis, a horizontal line can be drawn from the saturation region of the curve denoted VGS =0 V to the ID axis.
The resulting current level for both graphs is IDSS.
The point of intersection on the ID versus VGS curve will be as shown since the vertical axis is defined as VGS = 0 V.
When VGS = 0 V, ID = IDSS.
When VGS = VP  ID = 0 mA.

## Slide 37
The transfer characteristics are a plot of an output (or drain) current versus an input-controlling quantity.
There is therefore a direct “transfer” from input to output variables when employing
the curve to the left of prev. plot.
If the relationship were linear, the plot of ID versus VGS would result in a straight line between IDSS and VP.
However, a parabolic curve will result because the vertical spacing between steps of VGS on the drain characteristics of Fig. decreases noticeably as VGS becomes more and more negative.
Compare spacing between VGS = 0 V and VGS = 1 V to that between VGS=3 V and pinch-off. The change in VGS is the same, but the resulting change in ID is quite different