## Slide 1: Operational Amplifiers

## Slide 2: Op-Amp – The Surface
An Operational Amplifier (Op-Amp) is an integrated circuit that uses external voltage to amplify the input through a very high gain.
We recognize an Op-Amp as a mass-produced component found in countless electronics.
Fig (1) OPAMP IC and Pin Configuration

## Slide 3: What is an Op-Amp? – The Inside
Op-amps (amplifiers/buffers in general) are drawn as a triangle in a circuit schematic
The actual count varies, but an Op-Amp contains several Transistors, Resistors, and a few Capacitors and Diodes.
For simplicity, an Op-Amp is often depicted as follows which has minimum of five terminals such as inverting input, non inverting input ,power supply and an output.
Non-Inverting Input
Inverting Input
Positive Power Supply
Negative Power Supply
Output
divot on pin-1 end

## Slide 4: Basic Block Diagram of Op-Amp
An Op-Amp can be conveniently divided in to four main blocks
An Input Stage or Input Diff. Amp.
The Gain Stage
The Level Translator
An Out put Stage
Input Stage
(Diff. Amp.)
Gain Stage (C E Amp.)
Level Shifter
Out put Stage (Buffer)
V1
V2
VO
Op-Amp IC
I/P

## Slide 5: Basic Block Diagram of Op-Amp
A Differential Amplifier i.e, it is the input stage for the op-amp. It provides the amplification of the difference voltage b/w the two inputs.
A Voltage Amplifier(s) i.e, it is the second stage of op-amp

## Slide 6: Basic Block Diagram of Op-Amp
The internal op-amp formula is:
  Vout = gain(V+  V)
So if V+ is greater than V, the output goes positive
If V is greater than V+, the output goes negative
A gain of 200,000 makes this device (as illustrated here) practically useless

+
V
V+
Vout

## Slide 7: Ideal Op-Amp
The Ideal Op-Amp
It has infinite voltage gain and infinite bandwidth.
It has infinite input impedance (open) so that it does not load the driving source.
It has zero output impedance.
These characteristics are illustrated in figure. The input voltage ,Vin , appears b/w the two terminals, and the output voltage is AvVin , as indicated by the internal voltage source symbol.

## Slide 8: Op-Amp Parameters
Common Mode
Two signal voltages of the same phase, frequency and amplitude are applied to the two inputs as shown is given in below figure.
This results in a zero output voltage (as difference is 0V).
This action is called common-mode rejection.

## Slide 9: Op-Amp Parameters
CMRR (COMMON MODE REJECTION RATIO):
Desired signals can appear on only one input or with opposite polarities on both input lines. These desired signals are amplified and appear on the output.
Unwanted signals (noise) appearing with the same polarity on both input lines are essentially cancelled by the op-amp and don’t appear on the output. The measure of an amplifier’s ability to reject common-mode signals is a parameter called the CMRR (Common-Mode Rejection Ratio).
  The CMRR is often expresses in decibels (dB) as

## Slide 10: Op-Amp Parameters
INPUT OFFSET VOLTAGE
Ideal op-amp produces zero volts out for zero volts in.
However, in op-amp a small dc voltage, VOUT(error) , appears at the output when no differential input voltage is applied. Its primary cause is a slight mismatch of the base-emitter voltages of the differential amplifier input stage of an op-amp.
Input offset voltage, VOS ,is the differential dc voltage required between the inputs to force the output to zero volts.
Typical values of input offset voltage are in the range of 2mV or less. It is 0V in ideal case.

## Slide 11: Op-Amp Parameters
INPUT OFFSET VOLTAGE

## Slide 12: Op-Amp Parameters
INPUT BIAS CURRENT
Input terminals of a differential amplifier are the transistor bases and therefore , the input currents are the base currents as shown in the figure.

## Slide 13: Op-Amp Parameters
INPUT OFFSET CURRENT
Ideally, the two input bias currents are equal and thus their difference is zero.
However, in a practical op-amp, the bias currents are not exactly equal.
The input offset current , IOS is the difference of the input bias currents expressed as an absolute value.

## Slide 14: Op-Amp Parameters
INPUT IMPEDANCE
The Differential input impedance is the total resistance between the inverting and non-inverting terminals as illustrated in figure (a). Differential impedance is measured by determining the change in bias current for a given change in differential input voltage.
The common-mode input impedance is the resistance between each input and ground and is measured by determining the change in bias current for a given change in common-mode input voltage shown in figure.

## Slide 15: Op-Amp Parameters
OUTPUT IMPEDANCE
The output impedance is the resistance viewed from the output terminal of the op-amp as shown in figure below

## Slide 16: Op-Amp Parameters
Slew Rate
The slew rate (SR) of an op-amp is the maximum rate at which the output voltage can change in response to input voltage.
When the SR is too slow for the input, distortion results.
For example when an input sine wave is applied to a voltage follower it produces a triangular output waveform.
The triangular waveform results because the op-amp simply cannot move fast enough to follow the sine wave input.
This happens because voltage change in the second stage ( Voltage Amplifier(s) ) is limited by the charging and discharging of capacitors.
The slew rate is expressed as :
SR = ∆VO/∆t
The unit of SR is volts per microseconds.

## Slide 17: Infinite Gain in negative feedback
Infinite gain would be useless except in the self-regulated negative feedback regime
  negative feedback seems bad, and positive good—but in electronics positive feedback means runaway or oscillation, and negative feedback leads to stability
Imagine hooking the output to the inverting terminal:
If the output is less than Vin, it shoots positive
If the output is greater than Vin, it shoots negative
  result is that output quickly forces itself to be exactly Vin

+
Vin
negative feedback loop

## Slide 18: Even under load
Even if we load the output (which as pictured wants to drag the output to ground)…
  the op-amp will do everything it can within its current limitations to drive the output until the inverting input reaches Vin
  negative feedback makes it self-correcting
  in this case, the op-amp drives (or pulls, if Vin is negative) a current through the load until the output equals Vin
  so what we have here is a buffer: can apply Vin to a load without burdening the source of Vin with any current!

+
Vin
Important note: op-amp output terminal
sources/sinks current at will: not like
inputs that have no current flow

## Slide 19: Positive feedback pathology
In the configuration below, if the + input is even a smidge higher than Vin, the output goes way positive
This makes the + terminal even more positive than Vin, making the situation worse
This system will immediately “rail” at the supply voltage
  could rail either direction, depending on initial offset

+
Vin
positive feedback: BAD

## Slide 20: Op-Amp “Golden Rules”
When an op-amp is configured in any negative-feedback arrangement, it will obey the following two rules:
  The inputs to the op-amp draw or source no current (true whether negative feedback or not)
  The op-amp output will do whatever it can (within its limitations) to make the voltage difference between the two inputs zero

## Slide 21: Inverting amplifier example
Applying the rules:  terminal at “virtual ground”
  so current through R1 is If = Vin/R1
Current does not flow into op-amp (one of our rules)
  so the current through R1 must go through R2
  voltage drop across R2 is then IfR2 = Vin(R2/R1)
So Vout = 0  Vin(R2/R1) = Vin(R2/R1)
Thus we amplify Vin by factor R2/R1
  negative sign earns title “inverting” amplifier
Current is drawn into op-amp output terminal

+
Vin
Vout
R1
R2

## Slide 22: Non-inverting Amplifier
Now neg. terminal held at Vin
  so current through R1 is If = Vin/R1 (to left, into ground)
This current cannot come from op-amp input
  so comes through R2 (delivered from op-amp output)
  voltage drop across R2 is IfR2 = Vin(R2/R1)
  so that output is higher than neg. input terminal by Vin(R2/R1)
  Vout = Vin + Vin(R2/R1) = Vin(1 + R2/R1)
  thus gain is (1 + R2/R1), and is positive
Current is sourced from op-amp output in this example

+
Vin
Vout
R1
R2

## Slide 23: Summing Amplifier
Much like the inverting amplifier, but with two input voltages
  inverting input still held at virtual ground
  I1 and I2 are added together to run through Rf
  so we get the (inverted) sum: Vout = Rf(V1/R1 + V2/R2)
    if R2 = R1, we get a sum proportional to (V1 + V2)
Can have any number of summing inputs
  we’ll make our D/A converter this way

+
V1
Vout
R1
Rf
V2
R2

## Slide 24: Differencing Amplifier
The non-inverting input is a simple voltage divider:
  Vnode = V+R2/(R1 + R2)
So If = (V  Vnode)/R1
  Vout = Vnode  IfR2 = V+(1 + R2/R1)(R2/(R1 + R2))  V(R2/R1)
  so Vout = (R2/R1)(V  V)
  therefore we difference V and V

+
V
Vout
R1
R2
V+
R1
R2

## Slide 25: Differentiator (high-pass)
For a capacitor, Q = CV, so Icap = dQ/dt = C·dV/dt
  Thus Vout = IcapR = RC·dV/dt
So we have a differentiator, or high-pass filter
  if signal is V0sint, Vout = V0RCcost
  the -dependence means higher frequencies amplified more

+
Vin
Vout
C
R

## Slide 26: Low-pass filter (integrator)
If = Vin/R, so C·dVcap/dt = Vin/R
  and since left side of capacitor is at virtual ground:
  dVout/dt = Vin/RC
  so
  and therefore we have an integrator (low pass)

+
Vin
Vout
R
C